## Slide 1: Earthquake Detection in a Static and Dynamic Environment Using Supervised Machine Learning and a Novel Feature Extraction Method

## Slide 2: abstrak
Mendeteksi gempa bumi menggunakan smartphone atau perangkat IoT secara real-time merupakan tugas yang berat dan menantang, tidak hanya karena dibatasi oleh masalah real-time yang sulit tetapi juga karena kesamaan sinyal gempa dan sinyal non-gempa (mis., Noise atau aktivitas lainnya). Selain itu, berbagai aktivitas manusia juga semakin mempersulit saat smartphone digunakan sebagai sensor pendeteksi gempa. Untuk itu, dalam artikel ini, kami memanfaatkan teknik pembelajaran mesin dengan fitur gempa daripada metode seismik tradisional. Pertama, kami membagi tugas deteksi menjadi dua kategori termasuk lingkungan statis dan lingkungan dinamis. Kemudian, kami secara eksperimental mengevaluasi berbagai fitur dan mengusulkan model dan fitur pembelajaran mesin yang paling sesuai untuk lingkungan statis guna mengatasi masalah komponen yang berisik dan mendeteksi gempa bumi secara real-time dengan tingkat alarm palsu yang lebih sedikit. Hasil eksperimen dari model yang diusulkan menunjukkan hasil yang menjanjikan tidak hanya pada dataset yang diberikan tetapi juga pada data yang tidak terlihat yang menunjukkan karakteristik generalisasi model. Terakhir, kami mendemonstrasikan bahwa model yang diusulkan juga dapat digunakan dalam lingkungan dinamis jika dilatih dengan kumpulan data yang berbeda.

## Slide 3: Pendahuluan
Due to the nature of earthquakes, significant research efforts have been made to develop real-time earthquake detection systems for disaster management. Earthquake fatal levels of motion can cause fatalities and damage in populated regions [1]. Because typical human structures are unable to resist large magnitude earthquakes, possible ways to overcome such fatalities are to build earthquake-resistant buildings or to take advantage of an Earthquake Early Warning (EEW) system that provides seconds to minutes of warning in advance, thereby allowing people to move to safe areas or shut down dangerous machinery. However, it is not only costly to construct earthquake-resistant structures but also difficult to build a highly accurate nationwide EEW system.
In recent years, emerging computing technologies such as mobile computing and Internet-of-Thing (IoT) systems equipped with various MEMS (Micro Electro Mechanical Systems) sensors (e.g., accelerometers, gyroscopes, GPSs), Wi-Fi, bluetooth, etc., have been widely adopted in the following areas: smart healthcare, intelligent transportation systems, smart buildings, and earthquake early warning systems [2,3,4,5]. In particular, the MyShake project [6] leverages mobile technologies to develop an earthquake early warning system that combines a seismic method and a machine learning (ML) technology. The system is installed on a volunteer’s smartphone and then detects earthquakes using an Artificial Neural Network (ANN). It is the first global earthquake detection system using a smartphone and machine learning technique.
Based on the available literature, we can divide IoT-based earthquake detection into two parts by applicability. A mobile-based earthquake early warning system uses low-cost MEMS sensors in a smartphone or an IoT device as a seismic sensor in a dynamic environment, while the stationary sensor-based early warning system uses a dedicated device as a seismic sensor in static (i.e., fixed) environment. The non-earthquake data in a static environment include internal and external noises. The source of internal noises mainly come from a sensor in which an accelerometer continuously captures some vibratory signals. The external noises come from outside of a sensor because of constructions, heavy-traffic roads, etc., near the installed sensor. In a dynamic environment, the variety of human activities become a major part of the non-earthquake data, which significantly affects the system performance, and thus the earthquake detection task using a low-cost sensor is very challenging. In this environment, training a machine learning algorithm is critical because of the activities whose frequency and amplitude patterns look like earthquakes.
In traditional earthquake early warning systems, because acceleration data recorded from seismic sensors installed nationwide are sent to a centralized server for earthquake detection, network and processing delays are inevitable. Because there are a few seconds between a P-wave and an S-wave (e.g., 10 s [7]) depending on the distance from an hypocenter [8,9], to reduce the blind area of earthquake early warning, on-site or standalone earthquake detection devices have been recently introduced [10,11,24]. However, because of the real-time processing requirement and resource constraints of a detection device, heavy computational methods and deep neural networks cannot be applied at the sensor side. Nevertheless, the final detection can be performed at the server-side through advanced detection algorithms, a simple detection algorithm with a few features that require light computations at a client-side to complete the detection procedure as soon as possible is required. Because an earthquake detection device can be operated in either a static or a dynamic environment, trivial statistical amplitude and frequency features are not suitable for such environments.
As a result, our focus is to improve a machine learning model for an earthquake alert device that we developed in our prior work to detect earthquakes in static and dynamic environments [10,11]. The device not only detects an earthquake but also sends an alert with earthquake response information to nearby smart devices such as smartphones, smart TVs, etc. As the device operates independently, without any Internet connection or collaborations with other alert devices, it needs a highly accurate earthquake detection algorithm. Because traditional methods to detect earthquakes such as STA/LTA have high false alarm rates, it is risky to use only one earthquake detection method for a standalone device. Thus, we use both traditional earthquake detection methods and emerging technologies together to decrease the chance of false alarms and increase the overall earthquake detection ability. In this article, we systematically compare different earthquake features and datasets representing static and dynamic environments for the earthquake alert device, and then, based on our experimental results, we propose a new earthquake detection model that can be used in both static and dynamic environments.
The rest of the article is structured as follows. Section 2 introduces our prior work and compares relevant research efforts. Section 3 explains the methodology used in the proposed work, while Section 4 discusses (in detail) the experimental work done. Finally, Section 5 concludes this article.

## Slide 4: Kajian Pustaka
Prior Work and Related Work
In this section, we introduce our prior work for earthquake detection using emerging technologies and then compare our work with related research efforts.
2.1. Prior Work
In our prior work [10,11], we developed an earthquake alert device that includes a 32 bit processor, Wi-Fi, bluetooth, a buzzer, an LED light, etc as shown in Figure 1; its hardware system is described in Table 1. To detect an earthquake, the earthquake alert device uses a machine-learning-based algorithm and then sends out an alert message to nearby devices such as smartphones, smart watches, AI speakers and home automation devices, using Bluetooth or Wi-Fi.

## Slide 5: Figure 1. The developed earthquake alert device.

## Slide 6: Table 1. Specifications of the developed earthquake alert device.

## Slide 7
The detection algorithm that we developed for the earthquake alert device is based on an artificial neural network (Artificial Neural Network) [12], which is a simple machine learning technique widely used in the last several decades. The used ANN model has three neurons in the input layer, five neurons in the hidden layer, and one neuron in the output layer as shown in Figure 2.

## Slide 8: Figure 2. The ANN model with three inputs with one hidden layer.

## Slide 9
The detection algorithm consist of four phases including feature extraction, pre-processing, training, and testing of a machine learning model. To detect earthquakes, we use three features including inter-quartile range (IQR), zero crossing rate (ZC), and cumulative absolute velocity (CAV), which are the same features used in MyShake [6]. IQR is the amplitude between 25% and 75% of the acceleration vector sum. ZC is a frequency measure that indicates the number of time that the signal changes its sign. CAV is a cumulative measure of amplitude of the vector sum of three component acceleration. Then, we use 2 s of a sliding window with a 1.5 s overlap window on the acceleration data to calculate these three features in real-time.
After the extensive experiments, we installed devices in 29 locations of three different cities and operated them for two months. Even though the model showed a high accuracy of over 95% in our experiments, we found a few false alarms throughout the real operation. Therefore, in this article, we carefully assess the performance of the earthquake detection model and test its added features to determine the best features for earthquake detection in our operational environments. In the rest of the article, we present our efforts on the development of various features for earthquake detection and experimental results.

## Slide 10
2.2. Related Work
Various monitoring systems leveraging mobile technologies have been proposed, such as eWatch, smartphones, and MEMS [13]. In particular, extensive research has been done on wearable IoT in healthcare. For example, eWatch [14] is an online activity recognition system that embeds four different sensors, i.e., an accelerometer, alight sensor, microphone, and thermometer. The system is very responsive and needs no wireless communication. Similarly, Kao et al. [15] have used a tri-axial accelerometer in a portable device that can be placed on the user’s dominant wrist to detect human activities, such as running, working, swinging, brushing teeth, knocking, walking, and hitting. The accelerometer of a smartphone has also been used for human activity recognition, such as walking, running, walking (fast and slow), climbing stairs (up and down), and excercising aerobatics [16]. In the literature, there are many applications that used a sensor-based monitoring system; however, these are beyond the scope of this article. Instead, we deal with the binary classification problem, and our goal is to detect earthquakes from the accelerometer data in which the rest of the data is the non-earthquake class, whether that includes human activity or noise.

## Slide 11
Traditional seismic detection involves computational methods such as Short-Term Average/Long-Term Average(STA/LTA), cross-correlation, and template matching [17,18,19,20,21]. These methods are useful but have certain limitations. For example, STA/LTA can detect earthquakes without prior knowledge of the event but can also produce false positives when the situation is more challenging, such as when it involves a low signal to noise ratio (SNR), overlapping events, and some cultural noise. Similarly, cross-correlation detects earthquake signals but is computationally expensive, while template-based matching is a powerful computational method but requires prior information. The above methods are mostly operational in the central system. Moreover, the computational methods do not exhibit any intelligent behavior and operate only on the fixed threshold values.
Recently, there have been research efforts to use MEMS-based sensors as seismic sensors due to their low computational power and cost. Specifically, the NetQuakes project developed by the United States Geological Survey (USGS) installed MEMS sensors around the world but mostly in California [22] and began to collect seismic data from them. Similarly, the following projects developed around the world use MEMS sensors; Home Seismometer Network (HSN) developed by Japan Meteorological Agency (JMA), Palert system developed by NTU(National University Taiwan), Community Seismic Network and Quake-catcher Network (QCN) developed by California Institute of Technology and Standford University, respectively [23,24,25,26].

## Slide 12
IoT systems for public safety are widely adopted, where the intelligence behavior of such sensors as MyShake, which combines machine learning with traditional STA/LTA algorithm, limit or exclude human intervention [27]. To our knowledge, this is the first globally used smartphone-based earthquake early warning system used in a dynamic environment. Besides, deep learning approaches have also been adopted to detect earthquakes offline or online at the server-side, such as searching seismic data, mining undetected earthquakes in the data archives, and finding the earthquake location [28,29]. In this article, our first goal is to improve the existing earthquake detection model’s performance in the static environment. The second goal is to evaluate the machine learning algorithms and feature sets (both existing and proposed) for sensor-side in the dynamic environment with a variety of human activities.

## Slide 13: Metode penelitian (point 1-3)
https://www.mdpi.com/1424-8220/20/3/800/htm#B6-sensors-20-00800

## Slide 14: 1
Langkah-langkah yang terlibat dalam metodologi yang kami usulkan adalah fitur ekstraksi, pre-proses, pelatihan, pengujian, dan validasi.
Ekstraksi
Dalam konteks deteksi gempa berbasis ML, amplitudo dan frekuensi adalah dua informasi penting di antara berbagai statistik sinyal akselerometer. Oleh karena itu, berdasarkan dua statistik ini, kami mengekstraksi fitur dari komponen X, Y, dan Z dalam domain waktu dan frekuensi. Fitur domain waktu mencakup fitur yang digunakan di MyShake dan fitur yang kami usulkan. Fitur MyShake adalah sebagai berikut.
IQR (Interquartile Range): IQR adalah rentang interkuartil Q3 – Q1 dari 3 komponen vektor jumlah VS
dimana X, Y, dan Z adalah komponen percepatannya.
CAV (Kecepatan Mutlak Kumulatif): Fitur CAV adalah ukuran kumulatif VS di jendela waktu dan dihitung sebagai
di mana s adalah periode waktu total dari jendela fitur dalam detik, dan t adalah waktu. Dalam pekerjaan ini, kami menggunakan jendela fitur dua detik.
ZC (Zero-Crossing): ZC adalah tingkat persimpangan-nol maksimum dari komponen X, Y, dan Z dan tingkat persimpangan-nol dari komponen X dapat dihitung sebagai:
dimana N adalah panjang total sinyal X dan 1R <0 adalah fungsi indikator.

## Slide 15: 2
Pre-Proses
Pra-pemrosesan melibatkan penyeimbangan kumpulan data dan penskalaan fitur untuk rentang dari 0 hingga 1. Penyeimbangan diperlukan karena kumpulan data yang tidak seimbang sangat mempengaruhi kinerja model pembelajaran mesin [34]. Dalam kasus kami, kumpulan data non-gempa (kebisingan dan aktivitas manusia) jauh lebih besar daripada kumpulan data gempa. Oleh karena itu, kami menggunakan algoritma clustering K-mean untuk menyeimbangkan dataset non-gempa [35]. Menggunakan K-Mean, cluster dari data non-gempa dibuat sesuai dengan jumlah total titik data gempa, dan kami menggunakan centroid dari cluster untuk merepresentasikan data non-gempa.
Selain itu, untuk meningkatkan kinerja prediksi dan mengurangi waktu pelatihan model, kami juga menskalakan titik data d ke kisaran 0 hingga 1 menggunakan min-max scaler sebagai berikut:

## Slide 16: 3
Model Pembelajaran Mesin
Algoritma ANN (Artificial Neural Network) dirancang untuk menyelesaikan tugas deteksi menggunakan fitur yang ada dan yang diusulkan.Untuk lapisan tersembunyi dan lapisan keluaran, masukan dari lapisan sebelumnya ke setiap node akan dijumlahkan terlebih dahulu dan kemudian dimasukkan ke dalam fungsi aktivasi sebagai berikut:
Di sini, w menunjukkan vektor bobot, d adalah vektor masukan, b adalah bias, y adalah keluaran dari simpul yang diberikan, dan ϕ adalah fungsi aktivasi non-linier. Fungsi sigmoid logistik digunakan sebagai fungsi aktivasi untuk hidden dan output layer, yang didefinisikan pada input d sebagai :
Struktur umum model ANN/JST.

## Slide 17: 4/hasil
Hasil dan Diskusi
Untuk mendapatkan perbandingan yang komprehensif, kami membandingkan fitur yang diusulkan dengan fitur yang ada di lingkungan statis dan dinamis. Karenanya, kami melatih model ANN dengan kumpulan data non-gempa berbeda untuk membedakan lingkungan.
Dataset
Dataset yang kami gunakan untuk melatih dan menguji model ANN berisi dua kelas data label. Satu kelas data adalah kumpulan data gempa bumi deret waktu, yang diunduh dari database National Research Institute of Earth Science and Disaster Prevention (NIED) dan USGS (United States Geological Survey).
Data gempa NIED diproses sebelumnya dan diubah menjadi unit (g). Tingkat pengambilan sampel dari semua data gempa adalah 100 Hz. Data disajikan dalam tiga kolom berjudul EW, NS, dan UD, dimana EW (Timur-Barat) dan NS (Utara-Selatan) adalah komponen horizontal, dan UD (Atas-Bawah) adalah komponen vertikal.
Performance-Matriks
Algoritme pembelajaran mesin yang berbeda dievaluasi dengan matriks kinerja yang berbeda. Metrik kinerja klasifikasi didasarkan pada matriks konfusi [47], yang memberikan tabel TP (True Positive), TN (True Negative), FP (False Positive), dan FN (False Negative). Ukuran kinerja umum dari klasifikasi seperti akurasi, presisi, dan perolehan, dihitung dari matriks kebingungan. Akurasi dihitung sebagai:
Akurasi adalah rasio observasi prediktif dengan total observasi; ini adalah ukuran intuitif untuk menunjukkan kinerja model secara keseluruhan. Presisi dihitung sebagai:
Ukuran presisi menentukan seberapa akurat model dari prediksi positif tersebut. Dengan kata lain, berapa banyak dari mereka yang sebenarnya (dengan benar) positif di antara semua positif prediktif. Presisi tinggi berarti rasio positif palsu yang rendah. Perolehan dihitung sebagai :
Perolehan menentukan sensitivitas model dalam hal berapa kali ia mendeteksi gempa bumi dari semua kejadian gempa bumi.
Skor F1 adalah skor tunggal presisi dan recall yang merupakan mean harmonis dari keduanya. Ini memperhitungkan positif palsu dan negatif palsu.

## Slide 18: 5/ penjelasan tambahan
Evaluasi
Evaluasi dilakukan di lingkungan statis dan dinamis. Dalam lingkungan statis, sensor bersifat tetap (tidak bergerak) dan oleh karena itu, pelatihan model dengan variasi aktivitas manusia tidak diperlukan. Namun, untuk melatih model dengan benar untuk lingkungan statis, kami menggunakan beberapa contoh aktivitas manusia seperti berjalan dan menunggu. Hal ini karena model menyatu terlalu cepat dengan adanya data yang berisik saja sehingga tidak dapat mempelajari pola yang mendasari data tersebut, terutama pola gempa. Kami mengevaluasi model berdasarkan fitur yang berbeda dan kemudian, untuk lingkungan dinamis, kami menguji model yang menunjukkan hasil terbaik di lingkungan statis untuk mengevaluasi penerapan implementasi penuhnya.

## Slide 19: Hasil/kesimpulan dan saran
Dalam artikel ini, kami mengkategorikan mekanisme deteksi seismik ke dalam lingkungan statis dan dinamis dan kemudian mengevaluasi fitur yang berbeda menggunakan model ANN di lingkungan statis, yang mencakup fitur baru dan fitur yang sudah ada yang digunakan dalam studi sebelumnya. Berdasarkan hasil percobaan yang dilakukan di lingkungan statis yang dihasilkan, fitur yang diusulkan menunjukkan hasil yang lebih baik daripada fitur yang ada. Untuk lingkungan dinamis, kami menggunakan model yang sama yang diuji untuk lingkungan statis, kemudian melatihnya dengan kumpulan data berbeda, yang mencakup berbagai aktivitas manusia. Model yang dipilih menunjukkan hasil yang menjanjikan dengan kemungkinan alarm palsu yang lebih rendah dibandingkan model lainnya. Hasilnya, pendekatan kami dapat digunakan untuk lingkungan statis dan dinamis tanpa mengubah model dan fiturnya. Sebagai arah penelitian di masa mendatang, kami akan mengeksplorasi fitur dan model baru yang membutuhkan lebih sedikit daya komputasi sambil mempertahankan kemampuan deteksi tinggi terhadap kumpulan data non-gempa yang menantang.

## Slide 20: Kesimpulan dan Saran

## Slide 21: Tambahan penjelasan